## Slide 1
Belgrade, Montana
Established 2018
8-10 tons foodscraps / week
30 yards compost / month
1 Acre facility
Turned Windrows
Vermicomposting
Karl Johnson
Owner / Operator

## Slide 2
WARNING: This presentation is just a description of facility expansions / transitions, and a bunch of opinions about lessons learned. Skin your own cat
You are what you measure
Process and equipment
Nightmares Come True!!
Utilize Partnerships
Investing time vs. Spending time
Using Goals and Limitations to inform facility design and avoid debt

## Slide 3
Goals:
Create High Quality Products
Provide High Quality Service
Maximize Landfill Diversion
Limitations:
Don’t own Land
No Power at Site
Limited Access to Water
Cold Winter Temps
Semi-dispersed Service Area
Inexperienced Customers
High Labor Costs
Result:
Bucket Turned Windrows
Vermicomposting
Provide Collection Service
Include Bin Washing
But First . . .

## Slide 4
You Are what you Measure:
Process Consistency
=
Product Consistency
=
Repeat Customers
Outputs – Biology and Chemistry
Inputs / Recipe
Time is money – use a stopwatch, literally
As owner, value your own time (or at least track it) - eventually you’ll have to pay someone to do it
Labor cost vs. wage - 1.5 X – insurance, taxes
Price Services in order to afford expansion
Accounting Software
Cash Flow Spreadsheets

## Slide 5
First “windrow”
7 months of material
Composting:
1 ton / week
8-10 tons / week – active yard
Goals:
Maximize diversion
Limitations:
Don’t own Land
No Power at Site
Limited Access to Water

## Slide 6
Outdoor
Lower cost (rent + labor)
Mimic natural environment
Use Thermophilic heat for winter
???
Labor + Space
Heat and rent $$
Vermicomposting:
Goals:
Create High Quality Products
Limitations:
Cold Winter Temps
High Labor Costs
Winter
“CFT”
“worm bunker”

## Slide 7
Nightmare scenario!
Learn, then grow

## Slide 8
Collection:
Lift Gate!
Less trips =
Less fuel + labor
“Bucket Exchange” Kiosks
Goals:
Maximize diversion
Provide High Quality Service
Limitations:
Semi-dispersed Service Area
Cold Winter Temps

## Slide 9
Process and Equipment:
Buy used, no leaks!
Windrow “flipping”
< 200 lbs/week
???
Loader?
ASP?
Grants!!
Goals:
Maximize diversion
Limitations:
High Labor Costs

## Slide 10
“washhouse” / “wormhouse”
100 buckets / hour
30 buckets / hour
Goals:
Provide High Quality Service
Limitations:
Limited Access to Water (at compost yard)
Cold Winter Temps
Bin / Bucket Washing:

## Slide 11
$5000 (new)
$1200 down, balance financed through manufacturer over 12 months
Landlord’s tank and trailer
Fire Safety for property
$500 Honda 2” pump
Graywater!!
$500 trailer (new)
Used tank
$200 harbor freight 2” pump
Get Creative!
Goals:
Create High Quality Products
Limitations:
Limited Access to Water

## Slide 12
Partnerships – Mutual Benefits
All customers are Partners
Co-branding / advertising
Sustainability initiatives
Municipalities – it’ll happen eventually
  Lower cost service
  Diversion, lower quality products

## Slide 13
Investing time vs. Spending time –
Decrease Contamination through education
Make removal part of the process, don’t just rely on screening
Customer Feedback -
Pictures

## Slide 14
Stay curious and be willing to change
Kaizen – continuous evaluation and improvement
Use Data to inform decisions
Know before you grow
Don’t take yourself too seriously, you’re only saving the world, right!!??
Thank you!
Karl Johnson
406-219-7011
@yescompost
Yescompost.com
In other words: